## Slide 1: Drilling fluids – Recent and future research topics addressed at SINTEF
PIRE Project Annual Review Meeting June 18-20,
The City College of New York, CUNY
Presentation for Thrust III Drilling fluids.
Harald Linga, SINTEF
Notes: Bildet illustrerer:
· bredden i SINTEFs ekspertise, fra havrom til verdensrom.
· hvilke områder og bransjer vi jobber innen for å realisere visjonen Teknologi for et bedre samfunn.
Bildestilen er basert på stikkordene fremtidsrettet, teknologi og norsk natur (naturressurser). SINTEFs visuelle univers er utviklet for SINTEF av Headspin Productions AS.

## Slide 2
Content
Motivation & technology needs for drilling&well operations
Key features for drilling as a multiphase flow operation
Drilling & Well - SINTEFs profile and role
Selected projects, deliverables and results
Future topics
Slide 2

## Slide 3
Field development cost offshore – 40% related to drilling and well
Drilling performance decisive for investments/reservoir development
Proportion of mature, marginal fields are growing
More challenging drilling operations
  Extended Reach Drilling (ERD) - longer /deeper (8 km ++ )
  High Pressure High Temperature (HPHT) (800 bar ++, 150 C ++)
  Depleted reservoirs (pressure anomalies, loss of fluid)
  Exploration in arctic regions (topside temperature, HSE, logistics)
Slide 3
Motivation & technology needs for D&W operations

## Slide 4: Key features drilling; parameters and flow phenomena
QIN
QOUT
DIFFUSION
DYNAMIC INFLUX QRESERVOIR
QLOSS
CUTTINGS TRANSPORT
PHASE/PVT PROPERTIES drilling fluid/GAS/OIL/CONDENSATE
MULTI PHASE FLOW
HYDRATE
PARTICLE SAGGING
THERMOPHYSICAL PROPERTIES
RHEOLOGY(p,T,i)
DENSITY(p,T,i)
Drilling fluid COMPOSITION
MULTIPLE FLUIDS
GAS DISOLUTION IN drilling fluid
Colour legend:
RED: Real Time model RED & BLUE: Planning model VIOLET: Under development/Future
Drilling fluid characteristics and properties
essential for safe and efficient drilling performance
Notes: Colour of text distinguishes features that are available in real time and offline versions of the model, and features still not finished
Density and rheology are dependent on pressure, temperature, and fluid number (i)
Transient drilling operations means that model accounts for continuously changing pump rate, rotation rate, bit position, etc

## Slide 5
Rheology and non-Newtonian behavior; stability and model prediction performance, from turbulent flow to stagnant.
Narrow operating pressure window: ±2.5 bar bottomhole pressure accuracy at managed pressure drilling.
Interaction with rock/reservoir; particles & fluids
Complex composition, in the order of 10 constituents (fluids and weight material)
HSE performance; topside working environment and cutting discharge impact
Product cost, logistics and on-site preparation and monitoring
Drilling fluid regeneration and re-use
Slide 5
Drilling fluid design - concerns

## Slide 6
Slide 6
Drilling & Well - SINTEFs profile and role
R&D and advanced technical services within drilling, completion, well intervention and well integrity:
  Drilling dynamics and mechanics
  Hydraulics & Well Control
    Special solutions: Managed Pressure Drilling and Dual Gradient Drilling
  Monitoring & Control
  Well Integrity
  Well abandonment (P&A)
  Drilling and well for CO2 storage
  Drilling and well for geothermal energy
Example commercialized products; SINTEFs spin-off company eDrilling Solutions provide services for drilling and well simulator training and well planning.

## Slide 7: Activities, examples
Life-cycle well integrity
!
Integrated drilling simulator
Advanced interpretation of drilling data
: Managed Pressure drilling with drill string twist-off
Characterization of:
  Drilling fluids
  Crude oil
  Cement
  Emulsions
  Polymer solutions
  Other fluids
Notes: Life-cycle well integrity: The objective is to ensure well integrity throughout the life-cycle of the well.
Two main focus areas:
  Well barriers: Why do well barriers fail?
  Well design: To optimize well design with a life-cycle well integrity perspective in mind
Integrated drilling simulator: The heart of both the eDrilling system and the training simulator for drilling operations. IDS is a synthesis of multiple transient and steady state coupled models for the drilling sub-processes. It simulates interactions between the various sub-processes. At present the IDS consists of a dynamic flow and temperature model, a torque and drag model, a rate of penetration (ROP) model, a wellbore stability model, and a pore pressure model.
Advanced interpretation of drilling data: Advanced signal processing methods are used to detect upcoming problems at an early stage. As an example, poor hole cleaning can be detected by using time series prediction methods. Poor hole cleaning may result in low drilling efficiency, stuck pipe, problems with well control or even a loss of the wellbore. (The figure shows the output of an algorithm for early detection of poor hole cleaning. The algorithm gave warnings a couple of hours before the pipe got stuck. If the algortihm had been used during the operation this problem could have been avoided.)

## Slide 8: Key experimental facilities I; hole cleaning loop
Borehole flow loop for investigating hydraulic and friction issues behind drill bit
  12 m long, can be tilted to 30°
  Rotating steel string
  Compatible with any fluid system and any cutting type
  Measure pressure drop, torque, axial force and cuttings bed
Performance testing of different drilling fluids.
Interchangeable modules enable variations in wellbore diameter or geometry
Window for visual inspection or video

## Slide 9: Example 1: Lubricant added to drilling fluid
Impact from lubricant concentration
Type of drilling fluid; OBM/WBM
Drilling fluid flowrate
Friction factor calculated from measured torque
Parameter: Drilling string rotation
Friction vs. lubricant concentration at constant drilling string rotation
Motivation: Stuck pipe avoidance

## Slide 10: Example 2: Cuttings transport efficiency
Impact from drilling fluid flowrate
Type of drilling fluid; here OBM/WBM
Drilling string rotation
Cuttings content calculated from mass distribution/ load cells
Motivation: Stuck pipe avoidance
Cuttings hold-up vs. drilling fluid velocity in annulus

## Slide 11
Slide 11
Key experimental facilities II; rheology characterisation of gas saturated drilling fluids
Motivation: Reduce potentially large uncertainties in calculated bottom hole pressure, volume changes, and timing of gas flow rate to surface

## Slide 12
Example 1: Gas influx into drillling fluid, impact on viscosity
Slide 12
Viscosity decreases with increasing gas amounts
(methane loading as approach to equilibrium %)
Motivation:
Diagnosis of downhole pressure annulus pressure, risk for accelerated particle sagging

## Slide 13
SPE-180039-MS• Kick Detection Capability of Oil-based Muds in Well Control Situations • H. Linga
Example 2: Gas solubility and dense phase occurrence of drilling fluid-gas mixtures
Motivation:
Kick Detection Capability of Oil-based Muds in Well Control Situations
Henrys law loading characteristics until dense phase region is approached
Notes: Difference in density -> same %mass equals more CH4 absorbed in Sipdrill than EDC.

## Slide 14
Content
Motivation & technology needs for drilling&well operations
Key features for drilling as a multiphase flow operation
Drilling & Well - SINTEFs profile and role
Selected projects, deliverables and results
Future topics
Slide 14

## Slide 15: Future topics
QIN
QOUT
DIFFUSION
DYNAMIC INFLUX QRESERVOIR
QLOSS
CUTTINGS TRANSPORT
PHASE/PVT PROPERTIES drilling fluid/GAS/OIL/CONDENSATE
MULTI PHASE FLOW
HYDRATE
PARTICLE SAGGING
THERMOPHYSICAL PROPERTIES
RHEOLOGY(p,T,i)
DENSITY(p,T,i)
Drilling fluid COMPOSITION
MULTIPLE FLUIDS
GAS DISSOLUTION in drilling fluid
Colour legend:
RED: Real Time model RED & BLUE: Planning model VIOLET: Under development/Future
Particle sagging occurrence
Cutting transport performance
Gas – drilling fluid interaction
  kinetics (influx and degassing)
  rheology
  thermodynamics /phase envelope
Interpretation of along-string-measurements
  Hybrid analytics/machine learning
  Digitalisation
  Automated operations based on real-time downhole process condition diagnosis
Notes: Colour of text distinguishes features that are available in real time and offline versions of the model, and features still not finished
Density and rheology are dependent on pressure, temperature, and fluid number (i)
Transient drilling operations means that model accounts for continuously changing pump rate, rotation rate, bit position, etc